## Slide 1: TIME AND FREQUENCY CALIBRATION AND DISSEMINATION LABORATORY REQUIREMENTS
Raul F. Solis B.
CENAMEP AIP
Time and frequency Workshop

## Slide 2: Time and Frequency Laboratory
A typically time and frequency laboratory have 3 areas:
  Standards and traceability
  Calibration
  Dissemination
These areas always work together but calibration and dissemination depend of the work of the standards and traceability area.

## Slide 3: Standards
A time and frequency laboratory must have a reference and a mechanism to compare their signals with another laboratories.
The reference can be from a laboratory Quartz class to atomic clocks.
The comparison mechanism can be calibrations from another laboratory or a common view comparison.
But for the time and frequency laboratories that are the national reference, must have a good reference with common view comparisons to claim traceability.

## Slide 4: Calibration
Often, the laboratory calibration services cover:
  Frequency: Local oscillators, signal generator, frequency counters, etc.
  Time interval: clocks time differences, time interval generators, time interval counters, etc.
  Delays: cables, delay generators, etc.
These services can be cover with one or more devices in the laboratory.

## Slide 5: Calibration
Equipment often used in calibrations
  Frequency counter
  Time Interval Counter
  Signal generator
Equipment not regularly used to calibrate equipment but are necessary to control the process in the laboratory:
  Oscilloscope

## Slide 6: Dissemination
The process of dissemination can be related to the dissemination of:
  Time interval: 1 PPS, clock signals
  Frequency: 5 MHz, 10 MHz, etc.
  Time: NTP, web clock, etc.
Some dissemination technique are open to use and other must follow some recommendation (ITU R REC TF.374 “Precise frequency and time signal transmissions” or ITU R REC TF.768-6 “Standards frequency and Time signals”.

## Slide 7: Dissemination
The minimum equipment that you need to disseminate time interval signals is a Pulse Amplificator Distribuidor.
  Protect the 1 PPS output form your reference.
  Allow to have more than 1 output with the same metrological characteristic from the reference.
  Depending of the model, can transfer the 1 PPS to longer distances in the laboratory or another buildings.

## Slide 8: Dissemination
The minimum equipment that you need to disseminate frequency signals is a Signal Amplificator Distribuidor.
  Protect the frequency output form your reference.
  Allow to have more than 1 output with the same metrological characteristic from the reference.
  Depending of the model, can transfer the frequency signal to longer distances in the laboratory or another buildings.

## Slide 9: Dissemination
You can disseminate time with:
  NTP servers
  Web Clocks
  Telephone time server
But if you have the resources you can disseminate time using:
  Radio signals time code

## Slide 10: Dissemination
A web clock is a very striking way to disseminate the time and can be access by many people.
The problem is the code of the web clock and how the server will be on time.
A NTP server can solve this problem and allow to disseminate time in another way, but the cost of implement all these dissemination services can be more than USD 10 000.00

## Slide 11: Thanks rsolis@cenamep.org.pa