## Slide 1
Report on NIST activities
2017
Michael Lombardi

## Slide 2: OUTLINE
Contribution to Coordinated Universal Time (UTC)
Primary and Secondary Frequency Standards
Time Dissemination and Services
Advancing GPS and its applications

## Slide 3
Time and Frequency Distribution Services
Hydrogen Maser &
Measurement system
NIST Time and Frequency Standards and Distribution
Radio broadcasts
Networks
Satellites
Noise metrology
Primary Frequency Standards and
NIST Time Scale
Realization of SI second
NIST-F2
Research on Future Standards and Distribution
Optical clocks
Optical frequency
synthesis
Quantum computing
Chip-scale atomic devices

## Slide 4: UTC
UTC(NIST) is the local realization of UTC. The UTC(NIST) time scale consists of an ensemble of hydrogen masers and cesium clocks.
NIST maintains and operates UTC(NIST) and the U. S. Primary Frequency Standards, cesium fountain devices F1 and F2.
The time transfer links between NIST and BIPM are based on
  Two-Way Satellite Time and Frequency Transfer (TWSTFT) measurements utilizing geostationary satellites.
  GPS common-view measurements.
Coordinated Universal Time (UTC) is the official world time scale.
UTC is computed by the International Bureau of Weights and Measures (BIPM) in France.

## Slide 5: UTC
6 Hydrogen Masers
4 Cesium Beam standards
Measurement System
UTC(NIST)
Two-way satellite time & frequency transfer
GPS

## Slide 6: UTC
GPS: common-view
TWSTFT: Direct or indirect intercontinental satellite link
PTB is the pivot point for UTC
USNO shares with NIST the responsibility of maintaining accurate realizations of UTC in the US
SUV: TWSTFT mobile station owned by USNO, periodically driven to NIST in Boulder, CO
GPS with SUV cal: common-view calibration
CALIBRATIONS OF TIME TRANSFER LINKS

## Slide 7: UTC
BIPM issued updated Calibration Guidelines for all laboratories contributing to UTC
NIST (Boulder, CO, USA)
CNM (Queretaro, MEXICO)
CNMP (PANAMA)
INTI (Buenos Aires, ARGENTINA)
INXE (Rio de Janeiro, BRAZIL)
NRC (Ottawa, CANADA)
ONRJ (Rio de Janeiro, BRAZIL)
INM (Bogota, COLOMBIA)
INCP (Lima, PERU)
USNO (Washington, DC, USA)
APL (Laurel, MD, USA)
IGNA (Buenos Aires, ARGENTINA)
NRL (Washington, DC, USA)
ONBA (Buenos Aires, ARGENTINA)

## Slide 8: UTC
G2 CALIBRATION CAMPAIGNS
Trip 1:
NRC (Ottawa, CANADA)
Trip 2:
CNM (Queretaro, MEXICO)
CNMP (PANAMA)
Trip 3:
NRC (Ottawa, CANADA)
Trips 4-5:
INTI (Buenos Aires, ARGENTINA)
INXE (Rio de Janeiro, BRAZIL)
ONRJ (Rio de Janeiro, BRAZIL)

EARLY 2018
NIST Travelling System
COMPLETED!
COMPLETED!


COMPLETED!

## Slide 9: Frequency Standards
1 second is defined as the duration of 9,192,631,770 periods of the radiation corresponding to the transition between the two hyperfine levels of the ground state of the 133Cs atom.
Current accuracy (uncertainty):
3 x 10-16 second.
25 trillionths of a second per day.
1 second in 100 million years.
PRIMARY FREQUENCY STANDARD FOR THE UNITED STATES
NIST-F1 Atomic Fountain Clock
Re-evaluation of all systematic effects after move to new labs

## Slide 10: Frequency Standards
SECONDARY: OPTICAL
Al+ 1124 THz
Hg+ 1064 THz
Yb 520 THz
Ca 456 THz
Sr 429 THz
Cs 0.0092 THz
Ion Clocks
F1, F2
Neutral Clocks

## Slide 11: Frequency Standards
SECONDARY STANDARDS: OPTICAL CLOCKS
Al+ 1124 THz
Hg+ 1064 THz
Yb 520 THz
Ca 456 THz
Sr 429 THz
Ions
Neutrals
Sr or YB optical lattice clocks
Al ion logic clock
Δf/f ~ 6 x 10-18
Df/f ~ 8 x 10-18
Df/f ~ 10 x 10-18
Single Hg ion trap

## Slide 12: DISSEMINATION
NIST provides common-view GPS measurement systems to its remote customers, allowing them to compare their clocks to UTC(NIST) by using the GPS.
The common-view data is processed in real-time and shows the time or frequency difference between UTC(NIST) and the customer’s clock.
FMAS: reports frequency uncertainty to the customer
TMAS: reports time uncertainty to the customer
NISTDO: locks the customer’s clock (rubidium or cesium) to the UTC(NIST)
Customers can then show traceability to the International System (SI) of units through NIST.
TMAS FMAS NISTDO

## Slide 13: DISSEMINATION
Map of Common-View GPS Systems
(78 total systems deployed, 53 at customer sites and 25 in SIM Time Network)

## Slide 14: DISSEMINATION
A NISTDO is the station clock at WWVH in Kauai
The Boulder-Kauai baseline is long (5324 km) and Internet access at WWVH is through a satellite and is not always available.
Even so, the average time offset is near 0 and peak-to-peak time variations are usually within ±10 ns of UTC(NIST) in Boulder.

## Slide 15: DISSEMINATION
Chart: NIST FMAS/TMAS Customers by Sector
| Electronics and Instrument Manufacturers | Financial Markets / Stock Exchanges | U. S. Military | Aerospace | Defense Contractors | U. S. Government | Private Calibration Laboratories | Telecommunications | Nuclear Energy
 | 16 | 8 | 7 | 7 | 5 | 4 | 2 | 1 | 1

## Slide 16
Time By Radio: WWVB
WWVB low frequency broadcast of time code signals (60 kHz). Began broadcasting from Fort Collins, Colorado in 1963.

## Slide 17: NEW LABORATORIES
Time scale migration in process
Second TW station for link with USNO
Room-temperature fountain standard (F1)
Optical frequency standards and frequency comb
Optical fiber link between buildings (time scale)
Secondary time reference points (clock trips)

## Slide 18: EXPLORING NEW IDEAS
NIST is involved in the Air Force Research Lab program to support the Navigation Technology Satellite 3 (NTS-3), as well as possible future clocks for GPS.
The current clock technology is unlikely to be significantly improved
Terrestrial measured
13kg
< 30W
Volume ~ 1.3 * legacy KernCo
NTS-3
on-orbit goal
Laser-cooled Atomic clocks for GPS satellites
in space
KernCo

## Slide 19: Work in Progress
BIPM-sponsored pilot program with Beidou GNSS receiver for time transfer
Regular measurements of maser frequency using Yb optical clocks
Regular intercomparisons between optical clocks (Yb, Al and Sr)
First report of optical secondary frequency standards to BIPM
Atomic Clock Ensemble in Space (ACES): installation of Microwave Ground Terminal next spring

## Slide 20
THANK YOU!