## Slide 1: SIGNAL GENERATION AND MEASUREMENTS IN TIME AND FREQUENCY
Raul F. Solis B.
CENAMEP AIP
Time and frequency Workshop

## Slide 2: Signal in Time and Frequency Metrology
Signals: typically, electromagnetic oscillations that have an amplitude, frequency and waveform that we can measure.
  Amplitude: from mV to V.
  Frequency: from DC to optical region.
  Waveform: sine, square, triangular, pulse, etc.
Exist all kinds of signals, but in metrology of time and frequency we seek for these that represent their source and we can calibrate.

## Slide 3: Synchronization and Syntonization
Synchronization is the process of setting two or more clocks to the same time
  Clocks, time interval reference, telecommunication systems, digital systems, etc.
Syntonization is the process of setting two or more oscillators to the same frequency
  Disciplined oscillators (like GPSDO), radio and microwave links, etc.

## Slide 4: Synchronization
For the same sampling time (t) and fA=fB
  If ϕA = ϕB: Signals are synchronized
  If ϕA ≠ ϕB : Signals aren’t synchronized

## Slide 5: Syntonization
For the same sampling time (t)
  If fA = fB: Signals are syntonized
  If fA ≠ fB: Signals aren’t syntonized
Is not necessary that ϕA= ϕB

## Slide 6: Signal Generation
The signal generation can be based on:
  Fixed frequency (Oscillators, clocks, timebase).
  Variable frequency (Frequency synthesizer, waveform generators).
The generation of fixed frequency signals or variable frequency signals depend directly of the reference oscilator.

## Slide 7: Signal Generation
Is an instrument that can generate different frequencies and waveform using a local oscillator.
Normally they have timebase based on Quartz with the capability of be disciplined by an external frequency.

## Slide 8
Base de tiempo 10 MHz
Electrónica
10 000 000 Hz
10 000 000 Hz
10 000 000
Signal Generation

## Slide 9
Base de tiempo 10 MHz
Electrónica
10 000 000 Hz
20 000 000 Hz
20 000 000
X 2
Signal Generation

## Slide 10
Base de tiempo 10 MHz
Electrónica
10 000 000 Hz
50 000 000 Hz
50 000 000
X 5
Signal Generation

## Slide 11
Base de tiempo 10 MHz
Electrónica
10 000 000 Hz
5 000 000 Hz
5 000 000
÷ 2
Signal Generation

## Slide 12
Base de tiempo 10 MHz
Electrónica
10 000 000 Hz
1 000 000 Hz
1 000 000
÷ 10
Signal Generation

## Slide 13
Base de tiempo 10 MHz
Electrónica
10 000 000 Hz
42 123 456 Hz
42 123 456 Hz
÷ ?
x ?
Signal Generation

## Slide 14
Base de tiempo 10 MHz
Electrónica
10 000 004 Hz
10 000 004 Hz
10 000 000 Hz
Signal Generation

## Slide 15
Base de tiempo 10 MHz
Electrónica
10 000 004 Hz
20 000 008 Hz
20 000 000 Hz
X 2
Signal Generation

## Slide 16
Base de tiempo 10 MHz
Electrónica
10 000 004 Hz
80 000 032 Hz
80 000 000 Hz
X 8
Signal Generation

## Slide 17
Base de tiempo 10 MHz
Electrónica
10 000 004 Hz
5 000 002 Hz
5 000 000 Hz
÷ 2
Signal Generation

## Slide 18: Signal Generation
The signal generator depends of his reference oscillator, but an better external oscillator can improve the signal synthesis.
But for low frequencies, the equipment electronics and local oscillator is the major source of noise.
You can avoid some noises if you change the waveform:
  From sine to square or pulse.
But if you want low frequency signal with low noise, you need to acquire a signal generator with these characteristics.

## Slide 19: Signal Measurement in Time and Frequency Metrology
When we measure signal in time and frequency terms, we are looking for:
  Signal frequency.
  Time Interval difference of the signal and a reference.
And the objective from measure these variables is to obtain the stability and the frequency offset of the reference oscillator.

## Slide 20: Signal Measurement
Frequency measurement
  Frequency meters
  Frequency counters
Time Interval Measurement
  Time interval counter
All these measurements are basically the comparison of the oscillation of the local oscillator and the oscillator of the device under test.

## Slide 21: Signal Measurement
The amplitude and the waveform of the signal can affect the measure (frequency counters and time interval counters).
Frequency counters depend of a zero crossing point detector to count the frequency of the signals.

## Slide 22: Signal Measurement
Frequency meters measure frequency by comparing some relative deviation of their internal mechanism (capacitors, inductors, etc.)
Time interval counter depend of their internal oscillator to count the time between the start and stop.

## Slide 23: Signal Measurement
In frequency terms, you can do a measurement using:
  Direct frequency measures.
  Single mixer frequency measures.
  Double mixer frequency measures.
In terms of time interval, you can do a measurement using:
  Time interval measures.
  Phase difference measures.

## Slide 24: Signal Measurement
The time interval counter literally count pulses between two events.
Is often used to calibrate clocks.
OSC
START
STOP
t
f = 5 MHz
T = 200 ns
t = 5 x 200 ns = 1 µs

## Slide 25: Thanks rsolis@cenamep.org.pa